## Slide 1: interfacing electronic devices using Python and labphew
Aron Opheij
Experiment Design 2020 course
10-09-2020 Utrecht University
Version 0.2

## Slide 2: This lecture
Some philosophy of lab automation and structuring code
Introducing the labphew package (watching me)
Helping you fork and install the labphew package (together)
You exploring it yourself (if there is time)
Two important comments:
All of this is a work in progress
It’s ok if you don’t understand everything today. This lecture serves as an introduction, after which you can explore at your own pace and ask us for help

## Slide 3: Automating experimental setups
When doing experiments you may quite quickly find yourself wanting or needing to automate your experimental setup. Some possible reasons may include:
  You want to speed things up
  Certain actions have to be performed quicker than possible by a human
  You have to repeat something many times
  You want to prevent human mistakes (due to boring repetition)
To achieve this you’ll have to write code to control devices.

## Slide 4: A pitfall during development
You start with writing code to solve a small automation task (e.g. perform a single simple experiment with a single device).
Then it turns out you want to add complexity to the measurement procedure or the experimental setup (add more devices perhaps), and you add this to your code.
As this continues it becomes harder and harder to modify and maintain your code. It becomes harder for yourself to understand and impossible for someone else.

## Slide 5: The onion principal: layers
In order to write expandable code it is important to split your code up in (smaller) encapsulated chunks.
The classes of Object Oriented Programming (OOP) are perfectly suited for this purpose.
These chunks can act as layers of an onion, one building on top of the other.
These can then more easily be modified or exchanged without having to worry about other parts of the whole code.
It is not always obvious where and how to split code up. Try to think about: how much would the rest of my code have to change if I make changes to this section?

## Slide 6: intermezzo on classes
Python classes allow you to create an object that has internal memory (variables/attributes) and functionality (functions/methods)
These internal variables and functions can be accessed and executed. (Much like a measurement device)
Nomenclature (for when you get confused)
  What you define is called a class. It is basically a “type” (just like integer or string, but one that can be very complex)
  Only once you have typed a = 5, a is a variable of type integer
  In the same way you first need to “create an object of that class” or “instantiate the class”. b = MyClass(). Now b is an instance of MyClass or an object of class MyClass
  The ‘functions’ inside a class are called methods
  The ‘variables’ inside a class are often referred to as attributes (but be careful attribute is technically a broader term that also includes methods)

## Slide 7: Controller – Model – View in context of labphew
Controller
  Is specific to a device
  Contains code to communicate with the device and possibly other code to make interacting with the device easier
  Note for developers:
    There exist “message-based devices” for which all communication happens as text commands over serial communication and devices which have their own driver/dll (these often prove a bit more difficult) and devices without a computer interface but that you operate by changing a voltage for example (you then need a device for that)
    Often you can find that someone in the online community has already written something for a device. Otherwise you’re going to need the manual
Model
  Is specific to an experimental setup
  We call the classes inside a model Operator
  When creating the Operator object one would pass one (or more) controllers as input arguments. These are the devices used by the Operator to perform a scan/experiment
  The Operator should contain several “functions“ (methods):
    To connect to the devices (with the controllers it was given as input)
    Also to disconnect
    To run a scan (experiment) (there could be multiple of such functions for different scans)
    To save data
    For live plotting in a graphical user interface (if you need that)
View
  Allows you to interact with the Operator in a graphical user interface (GUI)
  This has two classes which we call: MonitorWindow (for continuous a live “plotting”) ScanWindow (for performing a scan)

## Slide 8: Controller – Model – View in context of labphew
Controller
  Is specific to a device
  Contains code to communicate with the device and possibly other code to make interacting with the device easier
  Note for developers:
    There exist “message-based devices” for which all communication happens as text commands over serial communication and devices which have their own driver/dll (these often prove a bit more difficult) and devices without a computer interface but that you operate by changing a voltage for example (you then need a device for that)
    Often you can find that someone in the online community has already written something for a device. Otherwise you’re going to need the manual
Model
  Is specific to an experimental setup
  We call the classes inside a model Operator
  When creating the Operator object one would pass one (or more) controllers as input arguments. These are the devices used by the Operator to perform a scan/experiment
  The Operator should contain several “functions“ (methods):
    To connect to the devices (with the controllers it was given as input)
    Also to disconnect
    To run a scan (experiment) (there could be multiple of such functions for different scans)
    To save data
    For live plotting in a graphical user interface (if you need that)
View
  Allows you to interact with the Operator in a graphical user interface (GUI)
  This has two classes which we call: MonitorWindow (for continuous a live “plotting”) ScanWindow (for performing a scan)

## Slide 9: Controller – Model – View in context of labphew
Controller
  Is specific to a device
  Contains code to communicate with the device and possibly other code to make interacting with the device easier
  Note for developers:
    There exist “message-based devices” for which all communication happens as text commands over serial communication and devices which have their own driver/dll (these often prove a bit more difficult) and devices without a computer interface but that you operate by changing a voltage for example (you then need a device for that)
    Often you can find that someone in the online community has already written something for a device. Otherwise you’re going to need the manual
Model
  Is specific to an experimental setup
  We call the classes inside a model Operator
  When creating the Operator object one would pass one (or more) controllers as input arguments. These are the devices used by the Operator to perform a scan/experiment
  The Operator should contain several “functions“ (methods):
    To connect to the devices (with the controllers it was given as input)
    Also to disconnect
    To run a scan (experiment) (there could be multiple of such functions for different scans)
    To save data
    For live plotting in a graphical user interface (if you need that)
View
  Allows you to interact with the Operator in a graphical user interface (GUI)
  This has two classes which we call: MonitorWindow (for continuous a live “plotting”) ScanWindow (for performing a scan)

## Slide 10: labphew demonstration
  Quick demonstration
  Explaining the layers
  How would you use it

## Slide 11: Getting your own “copy” to modify
Repository on github: https://github.com/SanliFaez/labphew
Forking it
Cloning it
Making a conda environment (and why)
Installing the package
Nomenclature (possibly not purely accurate, but descriptive):
repository: collection of files being tracked by git versioning software (git helps you maintain different versions, share them, merge them)
github / gitlab: online services to store a git repository. Sharing between people (or even just different machines) usually goes through the remote copy on github(/lab)
Cloning a repository: making a “copy” on your local machine that is “linked” to the remote
Forking a repository: making your own remote “copy” of another project (that is not tracked by the original versioning)
package: a collection of python files that belong together and can be installed as one (when developing a package it’s usually in a repository, like in our case)
Having multiple conda environments allows you to install/modify/remove packages without affecting the configuration in other environments and vice versa (note: virtualenv is another solution for python environments)

## Slide 12: Extra bits

## Slide 13: Tips for coding when collaborating
Always think about someone else having to look through your code In software companies (where code is read much more often than it’s written) this is crucial , but it will help yourself as well when you look at code you’ve written a year ago.
Use descriptive names for variables and objects.
Add in-code documentation to classes and their methods. Descipbe what they do. If copy the style used in labphew it is possible to build html documentation from that.
Comments in code can be good. Even better is to use logging statements (see labphew docs for explanation)

## Slide 14: Important links
The repository containing the package: https://github.com/SanliFaez/labphew
Documentation https://labphew.readthedocs.io/en/latest/index.html
The API documentation doesn’t work yet on readthedocs. You can get a copy from Teams and look at it locally: https://solisservices.sharepoint.com/sites/UtrechtExperimentDesign2020/Shared%20Documents/labphew/html.zip

## Slide 15
I understand you’ll be introduced to git more properly next week.
It is often very confusing to new users. The following slides contain my attempt to explain it

## Slide 16: Versioning with Git, basics
Git can keep track of file-changes in a folder. This folder is then referred to as a repository.
However it does not continuously store all changes. Once you’d like to commit to the changes you’ve made you need to tell git to do so.
To commit file changes you first need to tell git which file-changes you’d like to include. This is called staging.
Once file-changes are staged, they can be committed and become part of the stored history of the repository (“folder”). Each commit should be accompanied with a short message describing what changes are made.
(Note that it is possible to stage file-changes and make more changes to the same file. If you commit at that point, only the staged changes are committed)
You could think of Git as storing a long list of cumulative consecutive commits (“file-changes”) in a folder.
…

## Slide 17: Versioning with Git, branches
…
This main list of commits is usually referred to as the master branch. You can split off from this main branch into another branch. Meaning that these branches have a shared history up to the point where the split happens, and from there on they store their own new commits. This can be very useful when trying something out that you’re not sure yet you want to keep, or when working on one repository with multiple people.
One branch can be merged into another (i.e. the list of commits of one branch are added to another). For example this way you could add the things you’ve been working on in a separate branch into the master branch.
Note that if both branches contain commits that include changes in the same part of the same file, Git can’t decide which to choose and it tells you there’s a merge conflict. It will show the file with both versions of the conflicting parts and you need to pick what you want to keep (i.e. delete sections) . Solving merge conflict can be a pain and is best to be avoided. It takes a bit of discipline to prevent working on the same file in different branches.
…

## Slide 18: Versioning with Git, remote repository
…
To share code between multiple people (or even multiple computers of one user), it is convenient to store this repository on a server (e.g. website like Github or Gitlab) this is referred to as “remote” whereas your local copy is “local”. The remote becomes the central place for exchanging copies between multiple users/computers and is also referred to as “origin”.
You can push (the new commits of) your local branch to the origin. And you can pull (new commits of) a remote branch to your computer.
A pull can be done in two steps: first fetch (which retrieves the data from the server), followed by a merge of the remote version of the branch into your local version of the branch.
…

## Slide 19: Versioning with Git, tips
Keep your commits small and give them useful messages
When starting “something new” in your code, make a separate branch! It’s easier to keep your master branch clean while you try stuff out on the new branch. Especially if you only work on new files, merging won’t create conflicts
Don’t work on the same file in different branches! If you’ve made changes in branch A that you also want in branch B, you should merge branch A into B.
In general, but especially when working with multiple people on the same repository, it’s good practice to frequently pull changes from the master branch
Stay aware of what branch you’re working in
It’s a good habit to make sure your code doesn’t crash and commit it before stepping away for a long period. If you come back the next day (or several days later), it’s nice to have it in working order with a commit message you could read back, instead of having to figure out if these changes were valuable or should be trashed.